## Slide 1: Exercise 3 – FF
Build:
T-FLIP FLOP Submit files: TFF.v,TFF_sim_waveform.jpg
Test bench: TFF_tb.v

## Slide 2: D-FF example
Main Module
  module dff(output reg q, input wire c,d,e);
always @(posedge clk)
if (e)
q <= d;
endmodule

## Slide 3
Test bench:
module dff_test;
wire q; reg c,d,e; dff dffi(q,c,d,e);
task expect(input xq);
if (q!==xq) begin
$display("TEST FAILED");
$display("time=%0d d=%b e=%b q=%b",$time,d,e,q);
$display("q should be %b",xq);
$finish;
end
endtask
initial repeat (5) begin c=1; #1 c=0; #1; end
initial @(negedge c) begin
{d,e}=2'b01; @(negedge c) expect (0); {d,e}=2'b10; @(negedge c) expect (0); {d,e}=2'b11; @(negedge c) expect (1); {d,e}=2'b00; @(negedge c) expect (1); $display("TEST PASSED");
$finish; endendmodule

## Slide 4: T ff
If input T is high, the T Flip-Flop changes state ("toggles") at clock positive edge.
If the T input is low, the flip-flop holds it’s previous value.
T-FF Truth Table: d = q T [ in Verilog d = q ^ T ; ]
Alternatively, if T=1, Qnext <= !Q ; [ not in Verilog is ! ]
Run the Test Bench and verify correct operation.
T
Q
Qnext
1
0
1
1
1
0
0
0
1
0
1
0
d q
clk
nrst
T

## Slide 5: 7- Segment Decoder
Hex number
7-Segment
Decoder
4
7
0
1
5
4
6
2
3