## Slide 1: Exercise 4 – Data Memory
Build:
Data Ram Submit files: DataRam.v,DataRam_sim_waveform.jpg
Test bench: DataRam_tb.v

## Slide 2
32 X 32bit words SRAM.
Synchronous read and Synchronous write.
SRAM Initialized to all zeroes by Data_RAM.txt file.
Loading the file using the $readmemh system task. initial
$readmemh(“Data_RAM.txt ", data_RAM) ;
Write to several locations and read from them.
Use parameters for the main module as well for the test bench.

## Slide 3: Nrst
Implement the following different options:
Once nrst rise, all the memory initialize to zero, line after line, synchronic . Please note that this option is not reversible (the operation will continue also when nrst was changed to ‘0’)לא מפסיק לאפס כשיורד ל0
Only when nrst is ‘1’ the memory initialize to zero. Start from the first line, synchronic.מפסיק לאפס כשיורד ל0
Only when nrst is ‘1’ the memory initialize to zero. Start from the current address line, synchronic.לא צריך

## Slide 4: Data Memory
32 X 32bits
SRAM
dout
din
addr
1 כתיבה 0 קריאהwr
אם 0 לא ניתן לכתובen
clk
32
5
32
מאפס הכלnrst