## Slide 1: Exercise 7 – fsm
Design a car-lights controller, when the options are: no lights (000), turn right (001), turn left (010), hazard (011) and brake (100).
There are 6 lights in the car, 3 for each side.
When car turns right, the lights change as follows: 100 110 111, and when car turns left the lights change on the opposite way: 001 011 111 .
When pressed hazard, all the lights blink together.
When car brakes, all the lights are on constantly.

## Slide 2
Notes:
1. When car turns, the sequence of the lights cannot be interrupted till it reaches 111.
2. If there was no new input the last sequence starts again.
3. Use clock to move between states and at the beginning you must start the car.
Write a test bench and verify correct operation of the controller.

## Slide 3
ignite
left
left
left
No lights
left
right
right
right
No lights
right
right
left
Brake or hazard
Brake or hazard
No lights
Brake or hazard
left
right
hazard
hazard
brake
No lights